## Slide 1: Arduino – LED Blinker without delay()
Cluster Intermediate IOT
Adrian Gould
ICT50220 - Diploma of Information Technology
Notes: Based on:
Arduino Millis Tutorial - Millis() the Delay Killer - using millis() for timing instead of Delay (electronicshub.org)
Pushbutton and Flashing LED with mills() tutorial (baldengineer.com)
Alternate Blinking LEDs with millis() | Let's Start Coding | Coding for Kids (letsstartcoding.com)

## Slide 2: Create TinkerCAD circuit
Open TinkerCAD
Create the circuit as described below:
  Connect the ground rails together (black wire)
  Connect the positive rails together (red wire)
  Add one LED to a small breadboard
  Add one 500 Ohm resistor to the cathode of the LED
  Connect the other side of the resistor to a ground rail

## Slide 3: Create TinkerCAD circuit
… continued
  Connect the anode of the LED to Pin 3 on the arduino
  Add one pushbutton across the central channel
  Connect one 1K Ohm resistor to bottom left of pushbutton
  Connect the other end of the 1K resistor to the ground rail
  Connect the bottom right of pushbutton to positive rail

## Slide 4: Create TinkerCAD circuit
… continued
  Connect the top left of pushbutton to pin 8 on the Arduino
  Connect the positive rail to the 5V on the Arduino
  Connect the negative rail to a ground on the Arduino

## Slide 5: Create TinkerCAD circuit

## Slide 6: Write the Code to Blink
Blink the LED every second for one second:
const int ledPin = 3;
void setup()
{
pinMode(ledPin, OUTPUT);
}
void loop()
{
digitalWrite(ledPin, HIGH);
delay(1000);
digitalWrite(ledPin, LOW);
delay(1000);
}

## Slide 7: Blink LED when Pushbutton Down
Write the code to blink the LED when pushbutton pressed
#define SWITCH_PIN 8
#define LED_PIN 3
#define TIME_ON 1000
int switchState = 0;
void setup()
{
pinMode(LED_PIN, OUTPUT);
pinMode(SWITCH_PIN, INPUT);
}
void loop()
{
switchState = digitalRead(SWITCH_PIN);
if ( switchState == HIGH ) {
digitalWrite(LED_PIN, HIGH);
delay( TIME_ON );
digitalWrite(LED_PIN, LOW);
delay( TIME_ON );
}
}

## Slide 8: What’s the Problem?
What happens when you briefly press the button?
What happened when you press the button two or three times in one second?
What’s the problem?

## Slide 9: What no Delay?
How to remove Delay?
We will use
  millis()
  millis returns the number of milliseconds the code has been running
Time difference between calling ‘millis’ twice will help:
  Difference = Current ms – Previous ms

## Slide 10: What no Delay?
int period = 1000;
unsigned long time_now = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
if(millis() > time_now + period)
{
time_now = millis();
Serial.print("Time: ");
Serial.print(time_now/1000);
Serial.print("s - ");
Serial.println("Hello");
}
//Run other code
}
Create a new TinkerCAD
Name: InterRiot-NoDelay
Add the code shown
Open the Serial Monitor at the bottom of the screen
Run the simulation
What happens?

## Slide 11: Blinking no Delay!
Using the previous example
Let’s write our blink without using delay()

## Slide 12: Blinking without delay()
const int ledPin = 3;
int ledState = LOW;
unsigned long previousMillis = 0;
const long interval = 1000;
void setup()
{
pinMode(ledPin, OUTPUT);
}

## Slide 13: Blinking without delay()
void loop()
{
unsigned long currentMillis = millis();
if (currentMillis - previousMillis >= interval)
{
previousMillis = currentMillis;
if (ledState == LOW)
{
ledState = HIGH;
}

## Slide 14: Blinking without delay()
(continued from previous slide)
else
{
ledState = LOW;
}
digitalWrite(ledPin, ledState);
}
}

## Slide 15: Exercise
As with the “delay” version of blink…
  Add a check for the button press
  Blink LED for 1 second when pressed briefly
What happens when you press the button more than once quickly?

## Slide 16: END
Session 2